04 RSV Gearing

Top speed in 6th gear with stock 16/40 is no more than 10,000rpm, but often only 9700rpm.

# Sprockets 	Wheelbase   RPM@100kph  130kph      At 270kph

16/40 		Standard		3,600		4,700		9,750

16/42 		shorter		3,800		4,920		10,230

16/44		much shorter	3,970		5,150		10,700

15/40		longer		3,850		5,000		10,400

15/41		approx same	3,950		5,120		10,650

15/42		has about same wheel base and tops out at 265kph at 10700rpm

Note.

1. In standard 16/40 gearing it is not likely to be able to rev to over 9,750 in 6th (168mph/270kph). However it should rev to 10,700 or more in 6th with 15/41 gearing, so gearing down should not lose any top speed.
2. Although changing the final ratios does change the rev’s at a given speed, this is not the primary reason for achieving better acceleration. It is more to do with the ratios and the ‘thrust’ that they produce.
3. 15/41 is basically the same as 16/44, but 16/44 needs a longer chain. 
4. Altering your gearing does not effect yous speedo as it takes it's readings off a sensor at the rear wheel.
5. going to a 16/44 will require a longer chain. 16/43 MAY fit at a squeeze when new, but with some miles on the chain will have stretched a little and should fit.
6. Going to a smaller front sprocket will reduce your chain life a little. But if you want the higher gearing such as 15/41 or 16/44, it makes more sence to go 15/41 and just replace the front & rear sprocket as it is much cheaper than going 16/44 & having to replace the rear sprocket and the chain. Sure you will eventually have to replace the chain 1000 km sooner when you use the 15/41, but the 16/44 owner has to do the same very shortly too, and it will be their second replacement chain. I hope I explained that clearly.